## Slide 1
Model Identification: Comparison of Black-Box methods to identify the attitude dynamics of a quadrotor helicopter
Russo Alessio, Savaia Gianluca
School of Industrial and Information Engineering
Polytechnic of Milan
Prof. Lovera Marco ICT FOR CONTROL SYSTEMS ENGINEERING Milano - 2014/2015
https://github.com/rssalessio/ictproject

## Slide 2
Identify the attitude dynamics of a quadrotor helicopter using classical PEM methods.
Compare the results obtained with those obtained using subspace identification.
GOAL
DATA
Model identified with subspace methods.
Set of data measured during three experiments
TOOLS
Matlab
Github: https://github.com/rssalessio/ictproject (code available)
PROJECT GOAL

## Slide 3
Experiment
Data Proc. & Analysis
Model Identification
Validation
Already done
Should data be processed?
Is the model ok?
IDENTIFICATION CYCLE
IDENTIFICATION CYCLE

## Slide 4
EXPERIMENT

## Slide 5
EXPERIMENT
Three experiments, done in the following manner for
  For the system is closed loop, with a PD regulator and a certain reference
  For the system is in open loop, where is a PRBS (Pseudo random binary source) signal.
  For the system is again in closed loop.
Sampling time of input()/output() can see dynamics up to .
Experiment data is collected in a set , where is the i-eth experiment.
, where represents data for , etc… .
is the open loop data
EXPERIMENT

## Slide 6
EXPERIMENT DATA
EXPERIMENT

## Slide 7
DATA PROCESSING AND ANALYSIS

## Slide 8
When analysing data for black box modelling there are several steps to consider:
Is there any trend on the data (constant or linear) ? Detrend (not advisable if the system contains an integrator -> we lose dynamics
Analyse the covariance and spectrum of the input signal to understand the level of excitation
  We prefer signal that behave like WN to improve (identifiability ) the estimate of a parametric model
Estimate the impulse response and frequency response to gain:
  Insight into the system dynamics
  Estimation of the input dead time (time delay of the input)
DATA PROCESSING
AND ANALYSIS

## Slide 9
Input Covariance – Spectrum Analysis 1/5
DATA PROCESSING
AND ANALYSIS
Analysis of the covariance gives insight on the level of excitation of the input signal: for example we can run the Anderson Whiteness Test to understand if the input signal behaves like a random white noise.
Also the rank of the correlation matrix can give some info, but most of the time has a persistence of excitation very high:
  Matlab command pexcit always returned 50 (degree of persistence of excitation, its calculated based on min(n/3, 50) where n=rank(Ru) )

## Slide 10
Input Covariance – Spectrum Analysis 2/5
DATA PROCESSING
AND ANALYSIS
Ratio of violation | 1st Exp | 2nd Exp | 3rd Exp
Full data | 0.2245 | 0.2343 | 0.2231
1st portion | 0.3154 | 0.4293 | 0.4110
2nd portion | 0.1785 | 0.3049 | 0.2995
3rd portion | 0.4483 | 0.7414 | 0.9138
The following table summarise the results of the Anderson Test, with confidence 90%, considering all samples of each set.

## Slide 11
Input Covariance – Spectrum Analysis 3/5
DATA PROCESSING
AND ANALYSIS
1rd experiment, 2nd data set

## Slide 12
Input Covariance – Spectrum Analysis 4/5
DATA PROCESSING
AND ANALYSIS
1rd experiment, full data set

## Slide 13
Input Covariance – Spectrum Analysis 5/5
DATA PROCESSING
AND ANALYSIS
3rd experiment, full data set

## Slide 14
IMPULSE RESPONSE 1/3
DATA PROCESSING
AND ANALYSIS
Main two approaches to estimate the impulse response are:
Identify a FIR model
Make use of correlation analysis
From this we can make a rough estimation of the impulse response, and together with the measured data, try to estimate the input delay (dead time).
The correlation analysis works in the following way:
, suppose and causal filter, then consider (we still have the same impulse response if we apply the filter to both the signals):

## Slide 15
IMPULSE RESPONSE 2/3 – Estimation
DATA PROCESSING
AND ANALYSIS
First image is based on correlation analysis.
Second one is based on the identification of a fir model up to n=20.
Seems like that
A positive input
Is delayed of 2-3 lags (See confidence region)
Tested on all the datasets, quite similar behaviour.

## Slide 16
IMPULSE RESPONSE 3/3 – Data Analysis
DATA PROCESSING
AND ANALYSIS
Effect of u >0 after
2-3 Ts = 0.4-0.6 sec

## Slide 17
Model identification

## Slide 18
MODEL IDENTIFICATION - PEM
MODEL IDENTIFICATION
Based on PEM approach minimize a loss function (or a distance) function of,where is a function that predicts the value of based on past values of .
If fully describes the output
How to obtain In general we can describe a linear system in the following way:
Where are rational functions of , effectively defining then a lag operator, i.e:
Parametrised in
Then:

## Slide 19
MODEL IDENTIFICATION – WHICH MODEL
MODEL IDENTIFICATION
We don’t know G,H of the true system, neither its parametrisation, then how is built up in reality? (denote with the transfer functions of the true system, then:
  Define the numerator and denominator degrees of
  Define the parametrization of these rational functions
Based on this we get various models: ARX, ARMAX, OE, BJ, where the first one has the simplest dynamics, whilst the BJ model has the most complex dynamics.
Then we choose that gives the lowest values ofis the problem to solve.
In this project we are interested in simulation. In fact we want to find G s.t. How to address this problem with the minimization problem?

## Slide 20
MODEL IDENTIFICATION – WHICH MODEL
MODEL IDENTIFICATION
=
If we pose H=1 then we obtain a problem that address our project’s request (an OE model)
How good may be the the estimated G?
  Consider that y,u are correlated, there is a feedback
  We are also trying to estimate a noise (measurement noise, etc…) with the input u
Though we obtain the best G s.t.
Now, how to choose the cost function?

## Slide 21
MODEL IDENTIFICATION – LOSS FUNCTION
MODEL IDENTIFICATION
mean square error
= norm
norm of the uniform convergence
matlab fit function
For sure the 3rd cost function is the most unappropriate, since it tries to minimise the maximum error, which may be given by a noise peak.
Minimising the 4th or the 1st is the same since we are using the Euclidean norm, which minimise the variance of the error. Again, we may have peaks given by the noise, though if we have enough points may have no influence => global convergence.
The L^2 norm is simply the first cost function.

## Slide 22
MODEL IDENTIFICATION – LOSS FUNCTION
MODEL IDENTIFICATION
=
( and for the asymptotic pem theory we have uniform convergence for ) .
Unfortunately it’s a non linear problem, so we need iterative methods to solve the minimisation problem which is a derivation problem. We’ll come back on this later.

## Slide 23
How do we analyse the fact that we are using data measured in a closed loop system? Consider again
the original system without any assumption, with , where C is the controller, then:
Notice that 1+GC = S^-1, inverse of the sensitivity T.F.

## Slide 24
With our objective to obtain a simulated output very similar to the measurement (H=1) we obtain:
In order to understand the effect of the minimisation problem we can write in the following manner:

## Slide 25
MODEL VALIDATION
MODEL VALIDATION
but we are training a model based on data and then check the cost function on the same data -> we get a biased result.
To get unbiased results we need to test the cost function on a different data set.
Unfortunately in this project the data is quite similar, though the second data set covariance function is a little different We may test the cost function on a subset of this experiment.

## Slide 26
CONCLUSION
CONCLUSION & REMARKS

## Slide 27
WHAT WENT WRONG
AND WHY

## Slide 28
  CONCLUSION & REMARKS
Qui possiamo mettere tipo le ideee andate male o da provare
-interpolazione dati + training su essi
-experiment have the same kind of shape-> do an avg of the data and train
-use 2 experiments at time to do training and then validation on the other set