## Slide 1
Model Identification: Comparison of Black-Box methods to identify the attitude dynamics of a quadrotor helicopter
Russo Alessio, Savaia Gianluca
School of Industrial and Information Engineering
Politecnico di milano
Prof. Lovera Marco ICT FOR CONTROL SYSTEMS ENGINEERING Milano - 2014/2015
https://github.com/rssalessio/ictproject

## Slide 2
Identify the attitude dynamics of a quadrotor helicopter using classical PEM methods.
Compare the results obtained with those obtained using subspace identification.
GOAL
DATA
Model identified with subspace methods.
Set of data measured during three experiments
TOOLS
Matlab
Github: https://github.com/rssalessio/ictproject (code available)
PROJECT GOAL

## Slide 3
Experiment
Data Proc. & Analysis
Model Identification
Validation
Already done
Should data be processed?
Is the model ok?
IDENTIFICATION CYCLE
IDENTIFICATION CYCLE

## Slide 4
EXPERIMENT

## Slide 5
EXPERIMENT
Three experiments, done in the following manner for
  For the system is closed loop, with a PD regulator and a certain reference
  For the system is in open loop, where is a PRBS (Pseudo random binary source) signal.
  For the system is again in closed loop.
Sampling time of input()/output() can see dynamics up to .
Experiment data is collected in a set , where is the i-th experiment.
, where represents data for , etc… .
is the open loop data
EXPERIMENT

## Slide 6
EXPERIMENT DATA
EXPERIMENT
Experiments are quite similar, though the third one has some differences. For identification purposes we’ll see
That it’s better to consider the full set of an experiment than just a small set of it because of the number of data,
Despite the fact that we have 3 different stationary signals.

## Slide 7
DATA PROCESSING AND ANALYSIS

## Slide 8
When analysing data for black box modelling there are several steps to consider:
Is there any trend on the data (constant or linear) ? Detrend (not advisable if the system contains an integrator -> we lose dynamics
Analyse the covariance and spectrum of the input signal to understand the level of excitation
  We prefer signal that behave like WN to improve (identifiability) the estimate of a parametric model
Estimate the impulse response and frequency response to gain:
  Insight into the system dynamics
  Estimation of the input dead time (time delay of the input)
DATA PROCESSING
AND ANALYSIS

## Slide 9
Input Covariance – Spectrum Analysis 1/5
DATA PROCESSING
AND ANALYSIS
Analysis of the covariance gives insight on the level of excitation of the input signal: for example we can run the Anderson Whiteness Test to understand if the input signal behaves like a random white noise.
Also the rank of the correlation matrix can give some info, but most of the time has a persistence of excitation very high:
  Matlab command pexcit always returned 50 (degree of persistence of excitation, its calculated based on min(n/3, 50) where n=rank(Ru) )

## Slide 10
Input Covariance – Spectrum Analysis 2/5
DATA PROCESSING
AND ANALYSIS
Ratio of violation | 1st Exp | 2nd Exp | 3rd Exp
Full data | 0.2245 | 0.2343 | 0.2231
1st portion | 0.3154 | 0.4293 | 0.4110
2nd portion | 0.1785 | 0.3049 | 0.2995
3rd portion | 0.4483 | 0.7414 | 0.9138
The following table summarise the results of the Anderson Test, with confidence 90%, considering all samples of each set.

## Slide 11
Input Covariance – Spectrum Analysis 3/5
DATA PROCESSING
AND ANALYSIS
1rd experiment, 2nd data set

## Slide 12
Input Covariance – Spectrum Analysis 4/5
DATA PROCESSING
AND ANALYSIS
1rd experiment, full data set

## Slide 13
Input Covariance – Spectrum Analysis 5/5
DATA PROCESSING
AND ANALYSIS
3rd experiment, full data set

## Slide 14
IMPULSE RESPONSE 1/3
DATA PROCESSING
AND ANALYSIS
Main two approaches to estimate the impulse response are:
Identify a FIR model
Make use of correlation analysis
From this we can make a rough estimation of the impulse response, and together with the measured data, try to estimate the input delay (dead time).
The correlation analysis works in the following way:
, suppose and causal filter, then consider (we still have the same impulse response if we apply the filter to both the signals):

## Slide 15
IMPULSE RESPONSE 2/3 – Estimation
DATA PROCESSING
AND ANALYSIS
First image is based on correlation analysis.
Second one is based on the identification of a fir model up to n=20.
Seems like that
A positive input
Is delayed of 2-3 lags (See confidence region)
Tested on all the datasets, quite similar behaviour.

## Slide 16
IMPULSE RESPONSE 3/3 – Data Analysis
DATA PROCESSING
AND ANALYSIS
Effect of u >0 after
2-3 Ts = 0.4-0.6 sec

## Slide 17
Model identification

## Slide 18
MODEL IDENTIFICATION - PEM
MODEL IDENTIFICATION
Based on PEM approach minimize a loss function (or a distance) function of,where is a function that predicts the value of based on past values of .
If fully describes the output
How to obtain In general we can describe a linear system in the following way:
Where are rational functions of , effectively defining then a lag operator, i.e:
Parametrised in
Then:

## Slide 19
MODEL IDENTIFICATION – WHICH MODEL
MODEL IDENTIFICATION
We don’t know G,H of the true system, neither its parametrisation, then how is built up in reality? (denote with the transfer functions of the true system, then:
  Define the numerator and denominator degrees of
  Define the parametrization of these rational functions
Based on this we get various models: ARX, ARMAX, OE, BJ, where the first one has the simplest dynamics, whilst the BJ model has the most complex dynamics.
Then we choose that gives the lowest values ofis the problem to solve.
In this project we are interested in simulation. In fact we want to find G s.t. How to address this problem with the minimization problem?

## Slide 20
MODEL IDENTIFICATION – WHICH MODEL
MODEL IDENTIFICATION
=
If we pose H=1 then we obtain a problem that address our project’s request (an OE model)
How good may be the the estimated G?
  Consider that y,u are correlated, there is a feedback
  We are also trying to estimate a noise (measurement noise, etc…) with the input u
Though we obtain the best G s.t.
Now, how to choose the cost function?

## Slide 21
MODEL IDENTIFICATION – LOSS FUNCTION
MODEL IDENTIFICATION
mean square error
= norm
norm of the uniform convergence
matlab fit function
For sure the 3rd cost function is the most inappropriate, since it tries to minimise the maximum error, which may be given by a noise peak.
Minimising the 4th or the 1st is the same since we are using the Euclidean norm, which minimise the variance of the error. Again, we may have peaks given by the noise, though if we have enough points may have no influence => global convergence.
The L^2 norm is simply the first cost function.

## Slide 22
MODEL IDENTIFICATION – LOSS FUNCTION
MODEL IDENTIFICATION
=
( and for the asymptotic pem theory we have uniform convergence for ) .
Unfortunately it’s a non linear problem, so we need iterative methods to solve the minimisation problem which is a derivation problem.

## Slide 23
How do we analyse the fact that we are using data measured in a closed loop system? Is there a way to consider
The experiment an open loop experiment? We don’t know either the reference signal or the controller.
It is known, from the frequency analysis of PEM, that a fully modeled noise transfer function will give better results in
closed loop experiments when compared to OE models (where best means ), whilst OE models are the
best ones in OL experiments. In fact, from the identification experiments, BJ models had worse results compared
to OE models.
Moreover, we can assume that the quadrotor noise plus the measurement noise is little compared to the input signal.
Thus we can assume the experiment to have u and e uncorrelated => open loop experiment.

## Slide 24
Consider the following expression:
, if then the input signal And the error are uncorrelated, and:
, using the Parseval theorem:
If H=1 the minimisation of is given by the minimisation of For this reason the OE model yields better results.

## Slide 25
Can we apply a filter on data to improve the results? From the previous formula the frequency weighting is the
Following:
If we apply a filter on the data a factor L appears on the expression multiplying both terms. Notice that L
is s.t. .
Unfortunately, it’s difficult to obtain a filter expression for , therefore it’s easier to use a filter L s.t. . But,
Notice that the spectrum of u is quite flat, therefore it’s not a problem.
In this way all models converge to the OE ones.

## Slide 26
MODEL VALIDATION

## Slide 27
MODEL VALIDATION
MODEL VALIDATION
In order to validate a model, it is necessary to compare it with another set of data , since using again the training set would lead to non affordable (biased) results.
Unfortunately, as it is easy to see, all three sets are quite similar; because of this we cannot rely validation process only and further analysis are needed, even though it is a first step which allows us to have a impression.
As discussed in previous slides, there are many cost function we can make use of but in this project we have chosen the minimization of the simulation error
The validation will be performed in this way:
  Choose a model class
  Identify a model from one dataset using different order of complexity and keeping best fit
  Validate data on the other two dataset and write down results
  Repeat point 2. and 3. picking another dataset for training and the others for validation
  Repeat from point 1. with another model class

## Slide 28
MODEL VALIDATION - ARX
MODEL VALIDATION
*Training on 1 exp
A(z): 1 -1.9551 0.64593 0.70572 -0.41605 0.025549
B(z): 0 0 0.27464 -0.26442
Validation on 1 exp: 68.191 Validation on 2 exp: 63.8589 Validation on 3 exp: 86.9643
*Training on 2 exp
A(z): 1 -1.8858 0.50166 0.76105 -0.37101
B(z): 0 0 0.28013 -0.26904
Validation on 1 exp: 68.4208 Validation on 2 exp: 63.2204 Validation on 3 exp: 88.7234
*Training on 3 exp
A(z): 1 -1.8037 0.2948 0.93228 -0.41768
B(z): 0 0 0.17739 -0.033072 -0.1383
Validation on 1 exp: 67.6965 Validation on 2 exp: 62.7143 Validation on 3 exp: 85.5182

## Slide 29
MODEL VALIDATION - OE
MODEL VALIDATION
*Training on 1 exp
A(z): 1 -2.0798 1.5923 -1.0809 0.85391 -0.2781
B(z): 0 0 -0.17999 0.65694 -0.47025
Validation on 1 exp: 54.6866 Validation on 2 exp: 49.5952 Validation on 3 exp: 74.6829
*Training on 2 exp
A(z): 1 -2.046 1.4758 -0.99924 0.89773 -0.32148
B(z): 0 0 -0.19542 0.68029 -0.47878
Validation on 1 exp: 54.9233 Validation on 2 exp: 49.3283 Validation on 3 exp: 75.5403
*Training on 3 exp
A(z): 1 -3.7358 5.1579 -3.0089 0.49021 0.096966
B(z): 0 0 -0.077889 0.61883 -1.3542 1.1687 -0.35517
Validation on 1 exp: 58.1653 Validation on 2 exp: 49.5579 Validation on 3 exp: 62.7157

## Slide 30
MODEL VALIDATION
MODEL VALIDATION
OE performs better than ARX models as expected from the previous theoretical discussion.
ARMAX and BJ give exactly the same results as OE models using simulation focus. This is due to the fact that
Matlab uses a 2 step identification, where in the first steps assume the T.F. from e to y to be 1, to identify . Then
The T.F. from e to y is identified. Therefore we obtain the OE model for .
ARMAX and BJ give different results using prediction focus, but even with high complexity models they don’t get
As close as to the OE model. This might be a clue of being an open loop experiment since for closed loop data
Detailed T.F.s will give a better result (because of the compromise).
A deeper analysis can be done with a Matlab script we wrote (compareModels) which shows graphically the properties of the two models, as:
Simulated output compared to actual data
Spectra analysis
Absolute error: mean, variance and max
Covariance of simulation error
Anderson Test
Both models pass Anderson Whiteness Test but OE has a better fitting and less error variance.
See attached Matlab scripts for more detailed info.

## Slide 31
MODEL VALIDATION – DYNAMICS
Another way to discriminate among different models is to look at their dynamic behaviour.
Here we will analyze:
  Poles and Zero
  Step response
trying to understand which dynamic best suit the actual system.
We will also attempt to synthesize new models by shaping the pole-zero plot.
Each model class is trained using the three datasets with simulation focus, leading to three different models for each class. Model classes tested: ARX, OE.

## Slide 32
MODEL VALIDATION – DYNAMICS
ARX MODELS

## Slide 33
MODEL VALIDATION – DYNAMICS
OE MODELS

## Slide 34
MODEL VALIDATION – DYNAMICS

## Slide 35
MODEL VALIDATION – DYNAMICS
Looking at the step responses we can evaluate (roughly) the gain of the plant and use this piece of information to discriminate some models.
The third OE model has a quite long settling time which make us think that this model is not very reliable (indeed the third dataset gives very different result in every identification).
Overshoot is more significant (in percentage) in OE models rather than ARX ones.
Looking at zero-poles plot we can see that they are not very different, indeed in both ARX and OE we have the same set of zero and poles around .
The first and second ARX models are equal since we can cancel a zero in the origin and the pole close to it.
The first two OE models are very similar and they both have a zero outside the unit circle, which makes us think that an overparametrization might have occurred; in order to verify this option we can cancel that zero and see wheter or not the dynamics is somehow affected.

## Slide 36
MODEL VALIDATION – DYNAMICS
Step response leads to the same results and even the «compareModels» analysis tells us there is little difference in terms of absolute error.

## Slide 37
MODEL VALIDATION – DYNAMICS
The best way to constrast overparametrization is not shaping directly the zero-pole plot, but to perform another identification using a lower order.
We have then modified the identification script in order to see how much the variance of the simulation error varies among different orders. If there is little difference we will accept a worse performance in respect to a lower order.
A very good compromise in terms of performances has been found in the model OE33 which has always a zero outside the unit circle though.
We have then tried both to lower down the order of the identification and to cancel «by hand» that zero: the best is the former which still passes the Anderson Test.
In the next slide we show the comparison between the more complex OE35 and this OE23:
  A(z): 1 -2.6222 2.2976 -0.67315
  B(z): 0 0 0.11213 -0.10996

## Slide 38
MODEL VALIDATION – DYNAMICS
«compareModels» tells us the variance increases of one point only.

## Slide 39
CONCLUSION
We finally conclude by comparing our models with the one provided as reference (state-space).
The state space model is much more complex since it is a 5th order system (5 poles and 5 zeros) whilst our final choice is a 3rd order (3 poles and 2 zeros).
On the other hand it has a better fitting of the data, though the difference in terms of absolute error is minimal.
Also in terms of Error-to-Signal Ratio the state space is slightly better:
  SS55: 36,69%
  OE35: 37,87%
  OE23: 38,85%
In the next slides we show some graphical comparison of the two models.
CONCLUSION & REMARKS

## Slide 40
CONCLUSION
CONCLUSION & REMARKS

## Slide 41
CONCLUSION
CONCLUSION & REMARKS

## Slide 42
OTHER IDEAS

## Slide 43
  CONCLUSION & REMARKS
OTHER IDEAS
Non linear identification: tried to use matlab toolbox: Bad results
Interpolation of data, sampling at higher frequency, in order to obtain more training data: Bad results
Best result in terms of minimum variance found setting the input delay to 1: 5th order system with poles and zeros condensed in a small area, suggesting a bad identification.
Something more to try:
Instrumental variable method
New experiments including impulse and step response
Compare results with a physical model